## Slide 1
Fariha Ferdousi 1706143
Nausin Tabassum Kudrot 1706158
Sadia Afrose 1706161
Raisa Mashtura 1706163
Subah Karnine 1706174
Presenters:
Group 3
Sameia Zaman
Shahed-E-Zumrat
Md. Sadman Sakib
Presented To:
Intelligent Hand Gesture Based Security System

## Slide 2
The images show a snapshot of our hand taken from a mobile phone camera and the image processing output
About Our Project
Virtual security system
Opens door with a 5 digit password
The digits are read from hand gestures
Digit = number of fingers in a timeframe

## Slide 3
Why this project?
During a pandemic situation like in the current statusquo, minimizing human contact with machines is a goal
Safe althernative to retina scan or finger print based security system
Much less advanced technology needed compared to other security systems. Its also cost effective.
Easy implementation in real life
User can set and reset password whenever needed.
User friendly Security system
With hand gesture recognition, interaction with computer becomes easier.
Convenient for Disabled people

## Slide 4
Implements image processing and gives status as output to VSPE
MATLAB.
Virtual device creating virtual ports between MATLAB and Proteus
VSPE.
ARDUINO
Softwares Used
To capture video of hand gesture in real time
IP CAM APP
Programs Microprocessor in Proteus
PROTEUS
Main circuit implementation

## Slide 5
Image Processing
Images taken by IP cam
5 images taken
Extracting palm area
Hole filling and isolated object removal
Hand segmentation using binarization
Convert image to black and white fully
Getting number of fingers by palm area subtraction
Demonstrating the procedure
We have followed a number of steps to ensure maximum accuracy and minimum runtime.

## Slide 6
Hand Gesture Recognition In Real Time
This is an example of HGR used for device control. We use the following Matlab package to make our mobile camera act like an IP camera.
Counts number of fingers in Real Time.

## Slide 7
Hand Gesture Recognition In Real Time
Address of IP camera
After taking 5 counts the loop ends
Function returning a set of 5 digits
In between each data frame a pause of 6s is maintained

## Slide 8
Image Processing
Step One:
Binarization

## Slide 9
Image Processing
Step Two:
Hole filling and small area removal

## Slide 10
Image Processing
Step Three
Removing wrist area by erosion

## Slide 11
Image Processing
Step Four
Dilation of wrist area

## Slide 12
Image Processing
Step Five
Subtraction

## Slide 13
Image Processing
Step Six
Cleaning
Total number of separate areas are counted

## Slide 14
Starting Prompt:
Enter Password
Reset Password
User Manual: Starting the Programme
Enter Password:

## Slide 15
Starting the Programme
Reset Password:

## Slide 16
LIMITATIONS
Can not separate background objects
Shadows and bright flashes of light causes errors during binarization
Only one angle readable
Does not take position of finger into account
Arbitrary gestures can not be identified
Problems with using Image Processing

## Slide 17
Flow chart
Microprocesssor
Compare input arguments
Open the door for correct password
Display necessary message
VSPE
Take picture
Compare password
This flowchart demonstrates the procedure after obtaining the password input

## Slide 18
Virtual Serial Port Emulator (VSPE)
Two virtual ports are needed to establish connection between MATLAB and Proteus
COM2 and COM4 are two virtual ports are used to connect MATLAB and Proteus respectively.
VSPE CONNECTION:
VSPE is a software which is able to create various virtual devices to transmit/receive data.

## Slide 19
VSPE: Connecting MATLAB & Proteus
Initiate arduino communication
Sends variable content to arduino
Creates a serial communication object

## Slide 20
Arduino UNO PINOUT diagram

## Slide 21
Schematic Diagram
The hardware part of this project was simulated using Proteus
The components used are:
Microprocessor, ATEMEGA328P
COMPIM
LCD Display, LM016L
Logic Probe
Motor- PWMSERVO
POT- HG

## Slide 22
Microprocessor Programming
Microprocesssor ATMEGA328P is programmed using Arduino IDE.
Arduino takes input through the serial port connecting the microprocessor.
For correct input the servo motor turns 180 degrees and thus unlocks the door.
“Unlocked” is displayed on the LCD monitor
For incorrect input the servo motor does not rotate and thus the door remains locked.
“Wrong Password” is displayed on the LCD monitor

## Slide 23
Arduino Code (for correct password)

## Slide 24
Arduino Code (for incorrect password)
If input is any number other than ‘1’
sets the LCD cursor to the second line .

## Slide 25
Visual Representation
Door unlocked when correct password is entered
Door remains locked when incorrect password is entered

## Slide 26
The input output pins of Arduino are mapped with that of the microprocessor ATMEGA328P using the diagram shown on the left.
Pin Mapping

## Slide 27
Practical Implementation
of this project
A series of photo is taken by the IP camera and passed to a CPU connected to the security system
The MATLAB code is installed in the CPU
The MATLAB code analyses the input and passes necessary arguments to the microprocessor connected to the door circuit.
The microprocessor analyses the MATLAB command and unlocks the door if correct password is provided as input.

## Slide 28
Team Contribution
Raisa Mashtura- 1706163
Subah Karnine- 1706174
Fariha Ferdousi- 1706143
Nausin Tabassum Kudrot- 1706158
Sadia Afrose- 1706161
IMAGE PROCESSING
HARDWARE SIMULATION

## Slide 29
THANK YOU
THANK YOU!